## Slide 1
Analyzing the Benefits of More Complex Cache Replacement Policies in Moderns GPU LLCs
Jarvis (Yuxiao) Jia and Matthew D. Sinclair
University of Wisconsin-Madison
jia44@wisc.edu sinclair@cs.wisc.edu

## Slide 2
Background: m5 + GEMS = gem5
Classic: quick, simpler option
Often easier to configure
Only basic MOESI coherence protocol
Ruby: more sophisticated & adaptable
More in-depth coherence support
 | Ruby | Classic
Replacement policies | LRU, PseudoLRU | Random, LRU, TreePLRU, BIP, LIP, MRU, LFU, FIFO, Second-Chance, NRU, RRIP, BRRIP
Coherence protocols | MI_example, MESI_Two_Level, MOESI_CMP_directory, MOESI_CMP_token, MOESI_hammer, MESI Three Level, CHI, … | MOESI (snooping protocol)
Problem: Ruby cannot use state-of-the-art replacement policies in Classic
2

## Slide 3
Merging Replacement Policy Support
Merged the cache replacement policies from Classic to Ruby
Users can use any of the replacement policies in either model
3
How to validate correctness of replacement policies?

## Slide 4
4
Edge case example for SecondChance RP

## Slide 5
Access Pattern: A, C, E, G, A, C, I, K, A, C
Way1 Way2 Way3 Way4
5

## Slide 6
Access Pattern: A, C, E, G, A, C, I, K, A, C
Way1 Way2 Way3 Way4
Miss
6
A |  |  | 
0

## Slide 7
Access Pattern: A, C, E, G, A, C, I, K, A, C
Way1 Way2 Way3 Way4
Miss
7
A | C |  | 
0
0

## Slide 8
Access Pattern: A, C, E, G, A, C, I, K, A, C
Way1 Way2 Way3 Way4
Miss
8
A | C | E | 
0
0
0

## Slide 9
Access Pattern: A, C, E, G, A, C, I, K, A, C
Way1 Way2 Way3 Way4
Miss
9
A | C | E | G
0
0
0
0

## Slide 10
Access Pattern: A, C, E, G, A, C, I, K, A, C
Way1 Way2 Way3 Way4
Hit
10
A | C | E | G
1
0
0
0

## Slide 11
Access Pattern: A, C, E, G, A, C, I, K, A, C
Way1 Way2 Way3 Way4
Hit
11
A | C | E | G
1
1
0
0

## Slide 12
Access Pattern: A, C, E, G, A, C, I, K, A, C
Way1 Way2 Way3 Way4
Miss
12
A | C | I | G
0
0
0
0

## Slide 13
Access Pattern: A, C, E, G, A, C, I, K, A, C
Way1 Way2 Way3 Way4
Miss
13
A | C | I | K
0
0
0
0

## Slide 14
Access Pattern: A, C, E, G, A, C, I, K, A, C
Hit
14
A | C | I | K
1
0
0
0
Way1 Way2 Way3 Way4

## Slide 15
Access Pattern: A, C, E, G, A, C, I, K, A, C
Way1 Way2 Way3 Way4
Result: M, M, M, M, H, H, M, M, H, H
15
A | C | I | K
1
1
0
0

## Slide 16
Replacement Policy-specific Bugs (i.e., both Classic and Ruby)
  20881: MRU initialized replacement incorrectly
  20882: SecondChance initialized new entries incorrectly
  65952: FIFO incorrect if multiple new entries in same cycle
Integration with Ruby-specific Bugs (i.e., only in Ruby)
  21099: Ruby called cacheProbe twice in in_ports, causing RP info to be incorrect
  62232, 63191, 64371: Ruby updated RP info twice per miss, causing LFU, RRIP, and others to behave incorrectly (MI_example, MESI_Two_Level)
    This problem may be in other Ruby protocols too
Current Status: RPs have edge case tests integrated
  Correctness testing performed as part of gem5 regression testing
Turns Out The Replacement Policies Had Bugs!
16

## Slide 17
How Can We Use These Modern RPs in Ruby?
Prior work has not examined more complex RPs in GPUs
Conventional wisdom: LRU sufficient for GPUs
  Traditional GPGPU workloads have streaming access patterns
  GPGPU caches traditionally < 64B of space, on average, per thread
  Thus, unlikely data will remain in caches long enough for RP to matter
Modern GPUs used for an increasingly wide range of applications
These workloads reuse data more frequently
And modern GPUs have increasingly large LLCs
17
Added support to use these RPs in gem5’s GPU LLC

## Slide 18
Methodology
System Setup:
  Vega 20 GPU (60 Compute Units, 16KB L1 D$ per CU)
  L1 latency: 143, L2 latency: 260, Scalar cache latency: 167
    Latencies based on Daniel & Vishnu’s GAP work
Metrics:
  Vary L2 (LLC) cache sizes: [256KB, 512MB] (powers of two)
  L2 Replacement Policies: FIFO, LFU, LIP, LRU, MRU, NRU, SRRIP, SecondChance, TreePLRU
  Write-back and Write-through L2
Study of mix of streaming and non-streaming workloads:
  Pannotia, Rodinia
  Microbenchmarks to better trace access patterns
Show a subset of these results today for brevity
18

## Slide 19
Chart: 
| 256KB | 512KB | 1MB | 2MB | 4MB | 8MB | 16MB | 32MB | 64MB | 128MB | 256MB | 512MB
fifo | 12257969723 | 12224753528 | 12226494563 | 12221505668 | 12240011033 | 12171298702 | 12095756542 | 12084101542 | 12082738462 | 12082738462 | 12082738462 | 12082738462
lfu | 12213143483 | 12209825693 | 12206267588 | 12202303778 | 12199893968 | 12189692513 | 12197362058 | 12185024408 | 12082738462 | 12082738462 | 12082738462 | 12082738462
lip | 12258150653 | 12238645733 | 12245397863 | 12206030603 | 12234053663 | 12181445212 | 12095032267 | 12084101542 | 12082738462 | 12082738462 | 12082738462 | 12082738462
lru | 12258150653 | 12238645733 | 12245397863 | 12206030603 | 12234053663 | 12181445212 | 12095032267 | 12084101542 | 12082738462 | 12082738462 | 12082738462 | 12082738462
mru | 12245662598 | 12260343458 | 12247425278 | 12244069748 | 12232990838 | 12221262578 | 12223533638 | 12221141033 | 12082279477 | 12082738462 | 12082738462 | 12082738462
nru | 12257656703 | 12229774613 | 12222670613 | 12207715583 | 12220965098 | 12180478402 | 12095417437 | 12084101542 | 12082738462 | 12082738462 | 12082738462 | 12082738462
rrip | 12241183193 | 12233069093 | 12225235823 | 12203802278 | 12223629653 | 12148277857 | 12093427762 | 12082624132 | 12082738462 | 12082738462 | 12082738462 | 12082738462
second_chance | 12255974498 | 12229054778 | 12221264798 | 12211565618 | 12219782393 | 12178304467 | 12096168352 | 12084101542 | 12082738462 | 12082738462 | 12082738462 | 12082738462
tree_plru | 12238801688 | 12235799138 | 12229055888 | 12206107193 | 12228301088 | 12180559432 | 12096043477 | 12082858342 | 12082738462 | 12082738462 | 12082738462 | 12082738462
NW (Needleman–Wunsch) WT LLC Execution Time
LFU, MRU generally worse than others – Hurt temporal locality
Little difference between rest of policies until WS fits in LLC
19

## Slide 20
Chart: 
| 256KB | 512KB | 1MB | 2MB | 4MB | 8MB | 16MB | 32MB | 64MB | 128MB | 256MB | 512MB
fifo | 0.0041032 | 0.0066937 | 0.010311 | 0.017003 | 0.021368 | 0.031364 | 0.045115 | 0.047797 | 0.047117 | 0.047116 | 0.047116 | 0.047116
lfu | 0.00070592 | 0.0012467 | 0.002264 | 0.0036371 | 0.0045765 | 0.0055058 | 0.0091336 | 0.01416 | 0.047117 | 0.047116 | 0.047116 | 0.047116
lip | 0.0043465 | 0.0065133 | 0.010071 | 0.016757 | 0.020258 | 0.030254 | 0.04503 | 0.047797 | 0.047117 | 0.047116 | 0.047116 | 0.047116
lru | 0.0043465 | 0.0065133 | 0.010071 | 0.016757 | 0.020258 | 0.030254 | 0.04503 | 0.047797 | 0.047117 | 0.047116 | 0.047116 | 0.047116
mru | 0.00074108 | 0.0010991 | 0.0013976 | 0.0023787 | 0.0037258 | 0.0047088 | 0.0065702 | 0.010744 | 0.047105 | 0.047116 | 0.047116 | 0.047116
nru | 0.0040528 | 0.006657 | 0.010534 | 0.016741 | 0.020341 | 0.030169 | 0.045791 | 0.047797 | 0.047117 | 0.047116 | 0.047116 | 0.047116
rrip | 0.0042401 | 0.00663 | 0.010143 | 0.016746 | 0.019996 | 0.030001 | 0.042794 | 0.047457 | 0.047117 | 0.047116 | 0.047116 | 0.047116
second_chance | 0.0040782 | 0.0065597 | 0.010439 | 0.016976 | 0.0207 | 0.030987 | 0.04505 | 0.047797 | 0.047117 | 0.047116 | 0.047116 | 0.047116
tree_plru | 0.0044455 | 0.0066122 | 0.010272 | 0.016292 | 0.020128 | 0.030017 | 0.044622 | 0.047327 | 0.047117 | 0.047116 | 0.047116 | 0.047116
NW (Needleman–Wunsch) WT LLC Hit Rate
LLC Hit Rates confirm performance trends
20

## Slide 21
Chart: 
| 256KB | 512KB | 1MB | 2MB | 4MB | 8MB | 16MB | 32MB | 64MB | 128MB | 256MB | 512MB
fifo | 12157055182 | 12144287407 | 12132391536 | 12073462746 | 11946557000 | 11849261060 | 11581437484 | 10802967844 | 10732362410 | 10406127305 | 10398392270 | 10392605840
lfu | 12159421702 | 12147429262 | 12108004837 | 12116620101 | 12063551556 | 11929643931 | 11841167496 | 11815007016 | 12160463990 | 10393862360 | 10388636480 | 10406127305
lip | 12145707652 | 12145537267 | 12150849171 | 12063593736 | 11936668565 | 11869379255 | 11560805360 | 10728147184 | 10821811205 | 10398392270 | 10392605840 | 10421673965
lru | 12172320457 | 12146105587 | 12143672466 | 12063117546 | 11948208680 | 11879343725 | 11600751484 | 10722663784 | 10869453515 | 10424803055 | 10416009080 | 10388636480
mru | 12181225432 | 12191860897 | 12188160157 | 12179759676 | 12093317316 | 11982380586 | 11827687101 | 11795394981 | 10765827800 | 10420603370 | 10427412110 | 10392826730
nru | 12154053187 | 12157379302 | 12138524841 | 12048106461 | 11927281295 | 11841758570 | 11600266414 | 10753616689 | 10714911545 | 10399065485 | 10397109665 | 10392992120
rrip | 12150048862 | 12161191042 | 12133372776 | 12064801416 | 11906098610 | 11910473674 | 11546289889 | 10919456239 | 10841058605 | 10399065485 | 10423387250 | 10409649890
second_chance | 12146106142 | 12149096482 | 12141345351 | 12047986581 | 11920123460 | 11858249840 | 11547043025 | 10907854519 | 10756300670 | 10418429990 | 10392992120 | 10393862360
tree_plru | 12166078927 | 12161914762 | 12132200061 | 12063272946 | 11943572210 | 11839329890 | 11778663394 | 11330943229 | 10482640715 | 10426517450 | 10417038605 | 10421779415
NW (Needleman–Wunsch) WB LLC Execution Time
In general WB LLC caches outperform WT LLC caches – reuse opportunities
Average around 6% less execution time than WT
21

## Slide 22
Chart: 
| 256KB | 512KB | 1MB | 2MB | 4MB | 8MB | 16MB | 32MB | 64MB | 128MB | 256MB | 512MB
fifo | 0.00070293 | 0.00068 | 0.0027696 | 0.0062672 | 0.011646 | 0.015535 | 0.034667 | 0.077661 | 0.1124 | 0.11284 | 0.1125 | 0.1126
lfu | 0.00051771 | 0.00067575 | 0.0010817 | 0.0019194 | 0.0031271 | 0.0053036 | 0.012025 | 0.018042 | 0.11249 | 0.11251 | 0.11255 | 0.11284
lip | 0.00049053 | 0.00067116 | 0.0011399 | 0.0050112 | 0.011069 | 0.01105 | 0.032859 | 0.075261 | 0.11249 | 0.1125 | 0.1126 | 0.11337
lru | 0.0012677 | 0.00066033 | 0.0018965 | 0.0049116 | 0.01029 | 0.010931 | 0.032185 | 0.075582 | 0.11406 | 0.11319 | 0.11176 | 0.11255
mru | 0.00042881 | 0.00070396 | 0.0012663 | 0.0023468 | 0.003938 | 0.0080657 | 0.013363 | 0.017812 | 0.1114 | 0.11323 | 0.11337 | 0.11256
nru | 0.00074237 | 0.00074932 | 0.0026751 | 0.0071602 | 0.011611 | 0.014716 | 0.035332 | 0.077966 | 0.11248 | 0.1125 | 0.11247 | 0.11249
rrip | 0.00049609 | 0.00070148 | 0.0020395 | 0.0065192 | 0.011316 | 0.014451 | 0.035312 | 0.076607 | 0.11178 | 0.1125 | 0.11321 | 0.11178
second_chance | 0.00083825 | 0.00074429 | 0.0019829 | 0.0070094 | 0.010555 | 0.015264 | 0.034962 | 0.072061 | 0.11407 | 0.11324 | 0.11249 | 0.11251
tree_plru | 0.00066301 | 0.00072062 | 0.0025864 | 0.0066798 | 0.010141 | 0.014877 | 0.034787 | 0.073364 | 0.1132 | 0.11322 | 0.11177 | 0.11321
NW (Needleman–Wunsch) WB LLC Hit Rate
Same RP trends for WT caches (just hit rates vary)
Higher average hit rate than WT
22

## Slide 23
MRU and LFU generally perform worse than other RPs
WB/WT choice seems much more important than RP choice (besides not using MRU/LFU)
Performance affected less by RPs as cache size grows, fixed once WS fits in LLC
Surprising how little RP seems to impact performance
  Hypothesis: GPU Ruby protocols have similar RP update problems as Ruby CPU protocols
  Next Step: targeted microbenchmarks with known access patterns
Overall Result Takeaways
23

## Slide 24
Conclusion
Classic model has more complex RP support in gem5
  However, Ruby only supported LRU variants
We improved gem5’s publicly available RP support
  Merged RPs – Ruby can now use Classic’s advanced RPs
  Integrated RP edge case testing into gem5’s regression testing
  Added support to use these RPs into GPU
Current Results:
  MRU and LFU fail to exploit temporal locality (bad choices for GPU)
  Other RPs provide similar performance to one another
  WB vs. WT LLC seems to matter a lot more than RP choice
Next Steps:
  Use targeted microbenchmarks to debug GPU LLC RP behavior
  Integrate RP into known good GPU models
24